## Slide 1: CAEN 1260 Firmware

## Slide 2: Device Differences
1260
At UC Denver – using for dev
Designed for soft/firmware dev for 5560
2 LEMO input + 2 LEMO I/O
5560
At UMN – using for experiment
Designed for data collection
32 LEMO input + 2 LEMO I/O
Additional port types – USB, RJ45 (“SYNC”)
This presentation discusses firmware as built on the 1260 because the diagrams are simpler.
The 5560 firmware will function the same but have more channels and memory registers.
The 5560 is more powerful and has more clock options than the 1260.
  “Anything you can do, I can do better.”

## Slide 3
Input to 1260
Analog channels: Analog detector input
Many register values
  Set by utility programs (already written)
Output from 1260
LEMO 1: Timestamp formatted as LEMO trigger for DCRC
  Custom DCRC firmware by Sten
  Alternate version of towerfe3, towerfe3_NaI, built to save this stamp to data
LEMO 2/SYNC: Trigger pulse
  For diagnosis
All_Energies (Custom Packet): Data on pulse energies
  Collected + stored separately from Midas
  Matching timestamp

## Slide 4: Main Trigger Process
ANALOG IN CH 0
trig_low CH 0
trig_high CH 0
analog 0 > low trigger
analog 0 > high trigger
ANALOG IN CH 1
trig_low CH 1
trig_high CH 1
analog 1 > low trigger
analog 1 > high trigger
OR (low)
OR (high)
VETO
(low and not high)
Trigger
Notes: If this trigger is 1, then it tells the 1260 that an event has occurred and it should start sending and writing data.
Q/A: Technically there is an alternate trigger process – if(debug == 3){trigger manually each time `forcetrig` reg is set;}

## Slide 5: Basic Firmware Layout
Retrieve
Timestamp
DCRC triggers and saves timestamp
Integrate
CH 1
Integrate
CH 0
Custom Packet All_Energies
0x80000000
trigger_code
Generate
Trigger Code
timestamp
timestamp
0xc001
timestamp
energy_00
energy_01
Linux program reads & stores packet data
Trigger
Notes: Trigger code indicates which channels triggered. – Q/A These are represented as binary. Since the values are gated, it’s possible for multiple channels to trigger simultaneously.
0x80000000 is a header – Q/A: For the sake of alignment, if part of a packet is missing, it is a failsafe to tell us where the next packet begins so we don’t read part of the next packet as the end of this one.

## Slide 6: User-facing Programs
setregisters – Sets various registers, most notably detector enabling and thresholds.
scanrate – gets the rate at different lower thresholds and reports them back.
scanupper – gets the rate at different upper thresholds and reports them back.
scanwindow – gets the rate at different upper + lower thresholds of the same width and reports them back.
singlerate – gets the rate once, at current thresholds.
packettest – retrieves packet data with energies, timestamps, and trigger codes.
Notes: All programs have built-in help functions.
Underlined are the two programs I anticipate using during data collection.

## Slide 7: Running the acquisitions asynchronously
Advantages
No chance of bogging down MIDAS/CDMS DAQ, which runs many time-sensitive operations
Reduced development time
Minimal changes to CDMS DAQ required -> easy to go back to old version
Disadvantages
Two sets of data in different formats
Chance of “dead events” where one DAQ was running and the other was not.
Notes: What this means is that we essentially have two data acquisitions running asynchronously but simultaneously. One is the SuperCDMS DAQ and the other is a new, simple one for the CAEN device
Easy to go back to the old version of the CDMS DAQ if we need to, e.g. if we don’t want to use the NaI array for triggering for whatever reason

## Slide 8: Current Issues & To-Do
Timestamps are mostly similar, sometimes with a difference of 1, but
Many timestamps are lost or sent multiple times
Need to do more dev of the code that will zip the two datasets together
  It exists but it requires a lot of manual input or deletes too much data
Reduce time spent running the two programs non-simultaneously
  Results in “dead events” that can’t be aligned and complicate the alignment algorithm
Adjust packet retrieval program for continuous running
  Interruption does not cause graceful exit, kills 1 or more packets

## Slide 9: Backup Slides

## Slide 10: Basic Firmware Layout (Timing Details)
Trigger
Retrieve
Timestamp
DCRC triggers and saves timestamp
Integrate
CH 1
Integrate
CH 0
Custom Packet All_Energies
0x80000000
trigger_code
Generate
Trigger Code
timestamp
timestamp
0xc001
timestamp
energy_00
energy_01
Hold code
via gate
Hold timestamp
in FIFO
AND
data
ready
Linux program reads & stores packet data
Tell FIFO to send
Notes: 0x80000000 is a header – Q/A: For the sake of alignment, if part of a packet is missing, it is a failsafe to tell us where the next packet begins so we don’t read part of the next packet as the end of this one.

## Slide 11
R76Replica
https://github.com/villano-lab/NaI_Array_Firmware/tree/master/R76Replica

## Slide 12
R76Firmware
https://github.com/villano-lab/NaI_Array_Firmware/tree/master/R76Replica

## Slide 13: All Programs
setregisters – Sets various registers, most notably detector enabling and thresholds.
smalltest – Will not be ported to 5560; sets a small few registers and will be wrapped into setregisters.
getspectrum – non-functional. Should return spectra of integrated energies per channel. Instead returns un-/incorrectly-interpreted data.
  Abandoned because the packets give the same information in different format.
scanrate – gets the rate at different lower thresholds and reports them back.
scanupper – gets the rate at different upper thresholds and reports them back.
scanwindow – gets the rate at different upper + lower thresholds of the same width and reports them back.
singlerate – gets the rate once, at current thresholds.
teststatus – retrieves status information about various CAEN firmware functions.
packettest – retrieves packet data with energies, timestamps, and trigger codes.
fifotest – defunct. Retrieved a register (no longer exists) to verify data went into a FIFO.
fttest – Defunct. Tested possibility of connection using an alternate backend.
Notes: Bold: Fully functional or will continue to be developed.
Italic: used for debugging purposes
Underlined: used for main data collection
All programs have built-in help functions.